## Slide 1
Enable secondary CPUs in Bootloader
SCU enable
Initialization secondary CPUs
Set address for starting non-boot-cpu and
Set magic number to mark that will enable cpu
writel(init_secondary_cpu, SECONDARY_START);
337 writel(0xbabe, MAGIC_NUMBER);
Thread init
Thread initailization such as thread struct , stack and etc which is for only CPU#0
Assign start address to specify function pointer which will be called during setting up secondary cpu( init_secondary_cpu -> function pointer )
First boot
Check CPU id
Boot CPU is 0
Loop
All cores are reset, but boot core only initialized device.
Check if magic is marked.
If so execution is jumped to secondary start address.
In this case It is init_secondary_cpu.
Standby loop
Secondary start #3
Secondary start #2
Secondary start #1
Thread_init_per_cpu
Thread_init_per_cpu
Thread_init_per_cpu
Namely, Non-boot Cores are polling until the functions for secondary initialization is ready after RESET.

## Slide 2
Release secondary CPUs in Bootloader before jumping to kernel
Restore CPU function
Release Non boot CPUs
Thread finish
Boot CPU which is 0
Secondary CPUs are working in specific user function, so we need to restore the function pointer.
Check if magic is marked.
If so execution is jumped to secondary start address.
In this case It is init_secondary_cpu.
Standby loop
Thread work#3
Thread work #2
Thread work #1
exit
exit
exit
Kernel should assign proper init-function into the function pointer when secondary CPUS are in standby mode
Jump to kernel

## Slide 3
Enable secondary CPUs in Kernel & pen_release
Secondary_startup
smp_prepare_cpus(setup_max_cpus);
Smp_init
Loop
smp__ops.smp_prepare_cpus
Writing MAGIC number and secondary start address to the addresses which are same in bootloader, if settup is done PC is jump to the secondary start address
Secondary startup code is working like below.
1.Get current cpu id
2.Get current pen_release value
3.Compare cpud id with pen_release
4. If two values are same , jumping to secondary_startup which is setting PGD , enabling MMC for per CPU
Setup_arch
Smp_init_cpus
Smp_ops.smp_init_cpus which is setting up IPI caller . It is used to raise IRQ through IPI
Cpu_up
_Cpu_up
__Cpu_up
Boot_secondary
Smp_ops.smp_boot_secondary , it write CPUID into pen_release which triggers secondary_startup
After writing pen_release, it wait until the CPU is completely up, the CPU-UP is serialized.
__enable_mmu
__turn_mmu_on
__secondary_switched
Secondary_start_kernel
Cpu_idle_loop
CPU0 is waiting for all secondary CPUs-UP,
Sched_init_smp
Working in each CPU